Objectives

Reinforce good habits from previous lesson

Practice and improve maneuvers

Increase comfort in multitasking – control, planning, situational awareness, scanning for traffic, and communications

Begin work leading to approach, landing, and pattern

Steps/Schedule

Discussion – 0:15

Pre-flight – 0:15

Flight – 1:15

Post-flight discussion/Q&A – 0:15

Topics/Maneuvers

Ground reference maneuvers

Spin awareness

Approach and landing

Questions from last time

Equipment

- LA terminal chart – instructor

Ground reference maneuvers

3 maneuvers in PTS – generally asked to do 1 on checkride

- Develop skills needed for pattern work

- Visualization – putting the plane where it should be

- Wind correction – plane doesn’t always go where pointed

- Division of attention

For all of these maneuvers

- Ensure no other traffic nearby (clearing turns)

- Choose a legal altitude 600’-1000’ AGL

- Fly coordinated

- Look for traffic

- Target: altitude +/- 100’ and speed +/- 10 kts

- No more than 30 degree bank

Turns around a point

- Choose a specific point (landmark) for the center

- Enter on downwind with point ~½ mile off your left (why?)

- Fly a circle (not egg, spiral, or square) around the point

- Envision where the plane needs to be and make small corrections in bank angle to get there.

S-Turns

- Choose a straight line (road, track, or power line)

- Enter downwind perpendicular to the line

- Fly a half circle, arriving back perpendicular to the line with wings level (recommend a left turn first)

- Continue maneuver, fly equal half circle with a right turn

- Envision where the plane needs to be and make small corrections in bank angle to get there.

Rectangular course

- Choose a rectangle of roads

- Enter on downwind with the first road ½ mile off your left

- Maintain distance from the road, as you fly a rectangle

- Makes wind correction angle visible

Spin Awareness

What is a spin?

- Airplane descends quickly (> 2,000 fpm is common)

- Rotates quickly (>90 degrees/sec common)

- Can be very disorienting

- Unintentional spins are to be avoided, by avoiding unintentional stalls and proper technique during intentional stalls

- Intentional spins can be fun, with proper airplane and training

- Spin is not the same as a spiral

A spin requires

- Stall (though one wing is stalled more than the other)

- Yawing movement (being out of coordination)

Recovery from a spin - PARE

- Power off – power can make a spin worse

- Ailerons neutral

- Rudder opposite to direction of turn

- Elevator briskly forward to break stall

- Gently recover from resulting dive

Errors to avoid

- Attempting to make a sharper base to final turn using rudder

- Banking more than 30 degrees in the pattern

- Allowing airspeed to drop below recommended speeds in the pattern

- Uncoordinated stalls

Approach

A good approach is half the battle to a good landing

- Airspeed – find (and trim for) the pitch that gives the right airspeed

- Target point – initially use “the numbers” as your target

- Glide path – adjust power and flaps to establish proper glide path to the target

- Target dropping in field of view = overshoot, so decrease power or add flaps

- Target rising in field of view = undershoot, so increase power

- Keep direction of motion aligned down runway

Notes

Brackett airport in La Verne (KPOC) is a towered airport 13nm east of El Monte – usually the first airport we’ll visit besides El Monte

Terms/Acronyms

PAPI and VASI – both are lighting systems that give guidance on glide patch for landing, usually with a combination of red and white lights

Online Resources

http://flighttraining.aopa.org/students/presolo/skills/sturns.html

http://flighttraining.aopa.org/students/presolo/skills/rectangular.html